## Slide 1: Dairy Related Hoses
Hose Recommendations for the Dairy Industry

## Slide 2: RFFDAEOC Food Grade FDA Smoothbore EPDM Lined Red Smooth/Glossy Outer Convoluted Rubber Cover Hose
Tube: Smooth White EPDM, Phthalate Free REACH Compliant
Cover: Wide Corrugated FDA Rubber with Red, Low Friction, Smooth/Glossy, UHMW Cover
Reinforcement: Synthetic Plies, Steel Wire Helixes
Temperature Range: -40ºF to 245ºF (-40ºC to 118ºC)
Features:
  Lightweight
  Cover is abrasion, oil and chemical resistant
  Easy to clean

## Slide 3: RFFDAELF Food Grade FDA EPDM Rubber Lay Flat Hose
Tube: Smooth White EPDM
Cover: Grey EPDM Rubber
Reinforcement: Multi Textile Plies
Temperature Range: -20ºF to 300ºF (-29ºC to 149ºC)
Features:
  Tubing lays flat for easy storage
  Lightweight
  Available in bulk or fabricated lengths

## Slide 4: RFF&B Food Grade FDA Nitrile/PVC Blend Lined Food and Beverage Crush Resistant Hose
Tube: Smooth White Nitrile/PVC Blend
Cover: Grey EPDM Rubber
Reinforcement: Synthetic High Tensile Textile with Static Conductive Filament and Monofilament Helix
Temperature Range: -40ºF to 230ºF (-40ºC to 110ºC)
Features:
  Crush and kink resistant
  Chemical and ozone resistant
  Will not impart taste or odor

## Slide 5: RFFDABOC Food Grade FDA Smoothbore EPDM Lined Purple Smooth/Glossy Outer Convoluted Rubber Cover Hose
Tube: Smooth White Bromobutyl Phthalate Free
Cover: Corrugated Purple, Low Friction, Smooth/Glossy, UHMWPE Cover, Easy to Clean, Abrasion Resistant
Reinforcement: Synthetic Plies, Steel Wire Helix
Temperature Range: -40ºF to 250ºF (-40ºF to 121ºC)
Features:
  Extremely flexible
  Will not impart taste or odor
  Resistant to CIP solutions

## Slide 6: RFRTPOC Diversa-Flex™ Smoothbore PTFE Lined Hose with Blue Smooth/Glossy Outer Convoluted Rubber Cover Suction and Discharge Hose
Tube: Seamless white PTFE, phthalate free, REACH compliant
Cover: Wide corrugated FDA rubber with blue, low friction, smooth/glossy UHMW cover
Reinforcement: Synthetic plies, wire helixes
Temperature Range: -40ºF to 300ºF (-40ºC to 149ºC)
Features:
  Cover is abrasion, oil and chemical resistant
  Smooth glossy cover resists dirt and mold
  Easy to clean

## Slide 7: Certificates
3-A Sanitary Standards
USP Class VI