## Slide 1: Food Related Hoses
Hose Recommendations for the Food Industry

## Slide 2: RFFDAEOC Food Grade FDA Smoothbore EPDM Lined Red Smooth/Glossy Outer Convoluted Rubber Cover Hose
Tube: Smooth White EPDM, Phthalate Free REACH Compliant
Cover: Wide Corrugated FDA Rubber with Red, Low Friction, Smooth/Glossy, UHMW Cover
Reinforcement: Synthetic Plies, Steel Wire Helixes
Temperature Range: -40ºF to 245ºF (-40ºC to 118ºC)
Features:
  Lightweight
  Cover is abrasion, oil and chemical resistant
  Easy to clean

## Slide 3: RFFDAE Food Grade FDA EPDM Rubber Hose
Tube: Smooth White EPDM
Cover: Grey EPDM Rubber
Reinforcement: Two Polyester Spirals with Dual Helix Rubber
Temperature Range: -20ºF to 300ºF (-29ºC to 149ºC)
Features:
  Will not impart taste or odor
  Chemical and ozone resistant
  Abrasion resistant

## Slide 4: RFFDA Food Grade FDA Nitrile Rubber Hose
Tube: Smooth White Nitrile
Cover: White Nitrile Rubber (Abrasion and Oil Resistant)
Reinforcement: Two Polyester Spirals with Dual Helix Wire
Temperature Range: -40ºF to 180ºF (-40ºC to 82ºC)
Features:
  Abrasion resistant cover
  Will not impart taste or odor
  Chemical and ozone resistant

## Slide 5: RFRTPOC Diversa-Flex™ Smoothbore PTFE Lined Hose with Blue Smooth/Glossy Outer Convoluted Rubber Cover Suction and Discharge Hose
Tube: Seamless white PTFE, phthalate free, REACH compliant
Cover: Wide corrugated FDA rubber with blue, low friction, smooth/glossy UHMW cover
Reinforcement: Synthetic plies, wire helixes
Temperature Range: -40ºF to 300ºF (-40ºC to 149ºC)
Features:
  Cover is abrasion, oil and chemical resistant
  Smooth glossy cover resists dirt and mold
  Easy to clean

## Slide 6: Metal Detection Tube
Used as a metal detection machine component for viscous products such as liquids, slurries, syrups and pastes
Assemblies are manufactured using steam cleanable USDA, FDA approved schedule 80 PVDF pipe
Suitable for system temperatures of -40ºF to 240ºF (-40ºC to 115ºC) and 316L sanitary tri-clamp connections

## Slide 7: Sight Gauges
Used to view products and fluids flowing inline with rigid pipe lines
Available in a range of sight glass types including FEP, Polysulfone and Pyrex®

## Slide 8: Certificates
3-A Sanitary Standards
USP Class VI