## Slide 1: Pharmaceutical Related Hose
Hose Recommendations for the Pharmaceutical Industry

## Slide 2: RFRT Smoothbore FEP Lined EPDM Rubber Covered Hose
Tube: Seamless white FEP
Cover: EPDM rubber (abrasion resistant)
Reinforcement: Multiple braids, helical wire
Temperature Range: -40ºF to 300ºF (-40ºC to 149ºC)
Features:
  Liner is smoothbore FEP
  Non-Stick contact surface
  Ultra smooth bacteria free tube

## Slide 3: RFRTP Smoothbore Heavy Wall PTFE Lined EPDM Rubber Hose
Tube: Seamless white heavy wall PTFE
Cover: EPDM rubber (abrasion resistant)
Reinforcement: Multiple braids, helical wire
Temperature Range: -20ºF to 300ºF (-29ºC to 149ºC)
Features
  Resistant to ozone, chemical and abrasion
  Outstanding flexibility
  Ultra smooth bacteria free tube

## Slide 4: RFSTS Smoothbore PTFE Lined Hose with Stainless Steel Braided and Clear Silicone Outer Cover
Tube: Seamless White PTFE
Cover: Braided stainless Steel and clear silicone outer cover
Temperature Range: -20ºF to 350ºF (-29ºC to 176ºC)
Features:
  Silicone cover acts as thermal insulator
  Non-stick contact surface will not contaminate contacted substances
  Can be steam cleaned

## Slide 5: RFTFP – Tuf-Flex® Smoothbore PTFE Lined Hose with Synthetic Plies and Stainless Steel Wire Helix
Tube: Seamless White PTFE
Cover: White Silicone
Reinforcement: Synthetic Plies and Stainless Steel Wire Helix
Temperature Range: -40ºF to 300ºF (-40ºC to 149ºC)
Features:
  Superior cleanability
  Excellent thermal properties
  Ultra smooth bacteria

## Slide 6: RFSB Smoothbore Platinum Cured Silicone Hose with Braid Reinforcement
Tube: Smoothbore Platinum Cured Silicone
Cover: Platinum Cured Silicone
Reinforcement: Polyester Braid
Temperature Range: -100ºF to 350ºF (-73ºC to 176ºC)
Features:
  Ultra flexible
  Sterilizable by autoclave, CIP, SIP and gamma radiation processes
  Will not impart taste or odor

## Slide 7: RFSBX Medical Grade Smoothbore Peroxide Cured Silicone Hose with Braided Reinforcement
Tube: Smoothbore Peroxide Cured Silicone
Cover: Peroxide Cured Silicone
Reinforcement: Polyester Braid
Temperature Range: -80ºF to 350ºF (-62ºC to 176ºC)
Features:
  Translucent natural color for visual contact with the flow
  Will not impart taste or odor
  All ingredients are non-toxic and FDA sanctioned for use with food contact surfaces

## Slide 8: RFSBHP Smoothbore Platinum Cured High Pressure Silicone Hose with Double Braid Reinforcement
Tube: Smoothbore Platinum Cured Silicone
Cover: Smoothbore Platinum Cured Silicone
Reinforcement: Polyester Braid
Temperature Range: -100ºF to 350ºF (-73ºC to 176ºC)
Features:
  Smoothbore with braid reinforcement for increased working pressures
  Superior flexibility
  Hardness value: core – 70 Shore A, outer cover – 60 Shore A

## Slide 9: RFS4P Smoothbore Platinum Cured Silicone Hose with 4-Ply Reinforcement
Tube: Smoothbore Platinum Cured Silicone
Cover: Smoothbore Platinum Cured Silicone
Reinforcement: Polyester Brain
Temperature Range: -100ºF to 350ºF (-73ºC to 176ºC)
Features:
  Smoothbore with braid reinforcement for increased working pressures
  Superior flexibility
  Cleanroom manufacturing and packaged

## Slide 10: RFSV Smoothbore Platinum Cured Silicone Hose with Wire Reinforcement
Tube: Smoothbore Platinum Cured Silicone
Cover: Smoothbore Platinum Cured Silicone
Reinforcement: 4-Ply, Polyester Braid with Stainless Steel Helix Wire
Temperature Range: -100ºF to 350ºF (-73ºC to 176ºC)
Features:
  Ultra Flexible
  Hardness value of 70 Shore A
  Will not impart taste and odor

## Slide 11: RFSVOC Smoothbore Platinum Silicone Hose with Wire Reinforcement and Silicone Outer Convoluted Cover
Tube: Smoothbore Platinum Cured Silicone
Cover: Corrugated Platinum Cured Silicone
Reinforcement: 4-Ply, Polyester Braid with Stainless Steel Helix Wire
Temperature Range: -100ºF to 350ºF (-73ºC to 176ºC)
Features:
  Smooth inner bore
  Sterilizable by autoclave, CIP, SIP and gamma radiation
  Non-toxic

## Slide 12: Certificates
3-A Sanitary Standards
USP Class VI